## Slide 1: Process Selection and Facility Layout

## Slide 2
Introduction
Process selection
  Deciding on the way production of goods or services will be organized
Major implications
  Capacity planning
  Layout of facilities
  Equipment
  Design of work systems

## Slide 3
Process Selection
Variety
  How much
Flexibility
  What degree
Volume
  Expected output
Job Shop
Batch
Repetitive
Continuous

## Slide 4: Process Types
Job shop
  Small scale
  Low volume of high variety goods or services
  Skilled workers and general purpose equipment with high flexibility
  Eg-Doctor

## Slide 5
Batch
  Moderate volume
  Eg- bakeries which make breads, cakes or cookies in batches

## Slide 6
Repetitive/assembly line
  High volumes of standardized goods or services
  Slight flexibility of equipment is needed.
  Low skilled workers
  Eg- automobies, TV sets, automatic carwash.

## Slide 7
Continuous
  Very high volumes of non-discrete, highly standardized goods
  No variety in goods and no flexibility in the equipment
  Eg- sugar, flour, salt

## Slide 8: Product – Process Matrix
Dimension | Job | Batch | Repetitive | Continuous
Job variety | Very High | Moderate | Low | Very low
Process flexibility | Very High | Moderate | Low | Very low
Unit cost | Very High | Moderate | Low | Very low
Volume of output | Very low | Low | High | Very High

## Slide 9: Product and Service Processes
Process Type |  |  |  | 
Job Shop | Appliance repair Emergency room |  |  | Ineffective
Batch |  | Commercial baking Classroom Lecture |  | 
Repetitive |  |  | Automotive assembly Automatic carwash | 
Continuous (flow) | Ineffective |  |  | Steel Production Water purification

## Slide 10: Product and Process Profiling
Process selection can involve substantial investment in
  Equipment
  Layout of facilities
Product profiling: Linking key product or service requirements to process capabilities
Key dimensions
  Range of products or services that will be processed
  Expected order sizes
  Expected frequency of schedule changes

## Slide 11: Facilities Layout
Layout: the configuration of departments, work centers, and equipment, with particular emphasis on movement of work (customers or materials) through the system
    Product layouts
    Process layouts
    Fixed-Position layout
    Combination layouts

## Slide 12: Importance of Layout Decisions
Require substantial investment of money and effort
Involve long term commitments
Significant effect on cost and efficiency of operations

## Slide 13: Objective of Layout Design
Facilitate attainment of product or service quality
Use workers and space efficiently
Avoid accidents
Minimize unnecessary material handling costs
Eliminate unnecessary movement of workers or materials
Minimize production time or customer service time
Design for safety

## Slide 14: The Need for Layout Decisions
Inefficient operations
For Example:
High Cost
Changes in the design
of products or services
The introduction of new products or services
Accidents
Safety hazards

## Slide 15: The Need for Layout Design (Cont’d)
Changes in
environmental
or other legal
requirements
Changes in volume of
output or mix of
products
Changes in methods
and equipment
Morale problems
Eg-lack of face to face contact

## Slide 16: Basic Layout Types
Product layouts
Process layouts
Fixed-Position layout
Combination layouts

## Slide 17: Basic Layout Types
Product layout
  Layout that uses standardized processing operations to achieve smooth, rapid, high-volume flow
Process layout
  Layout that can handle varied processing requirements
Fixed Position layout
  Layout in which the product or project remains stationary, and workers, materials, and equipment are moved as needed

## Slide 18: Product Layout
Raw materials
or customer
Finished item
Station
2
Station
3
Station
4
Material
and/or labor
Station
1
Material
and/or labor
Material
and/or labor
Material
and/or labor
Used for Repetitive or Continuous Processing

## Slide 19: A U-Shaped Production Line
1
2
3
4
5
6
7
8
9
10
In
Out
Workers
Figure 6.6

## Slide 20: Process Layout
Dept. A
Dept. B
Dept. D
Dept. C
Dept. F
Dept. E
Used for Intermittent processing
Job Shop or Batch Processes
Process Layout
(functional)
Figure 6.7

## Slide 21: Process Layout
Process Layout - work travels to dedicated process centers
Milling
Assembly & Test
Grinding
Drilling
Plating

## Slide 22: Product Layout
Work
Station 1
Work
Station 2
Work
Station 3
Figure 6.7 (cont’d)
Product Layout
(sequential)
Used for Repetitive Processing
Repetitive or Continuous Processes

## Slide 23: Fixed Position Layouts
Fixed Position Layout: Layout in which the product or project remains stationary, and workers, materials, and equipment are moved as needed.
Nature of the product dictates this type of layout
  Weight
  Size
  Bulk
Large construction projects,aircrafts and rockets

## Slide 24: Design Product Layouts: Line Balancing
Line Balancing is the process of assigning
tasks to workstations in such a way that the workstations have approximately equal time requirements.

## Slide 25: Cycle Time
Cycle time is the maximum time
allowed at each workstation to
complete its set of tasks on a unit.

## Slide 26: Determine Maximum Output

## Slide 27: Determine the Minimum Number of Workstations Required

## Slide 28: Two Heuristic Rules

## Slide 34: Example-Positional Weight

## Slide 35: Calculating Positional Weight

## Slide 38: Final Solution