## Slide 1: Quality Control

## Slide 2: Phases of Quality Assurance
Acceptance
sampling
Process
control
Continuous
improvement
Inspection of lots
before/after
production
Inspection and
corrective
action during
production
Quality built
into the
process
The least
progressive
The most
progressive

## Slide 3: Inspection
Inputs
Transformation
Outputs
Acceptance
Sampling
(inspection before
production)
Process
Control
(inspection
During
Production)
Acceptance
Sampling
(inspection after
Production)

## Slide 4: How much to inspect and how often
Low cost, high volume items require little inspection and vice versa.
The amount of inspection depends on cost of inspection and the expected cost of passing the defective items.
With a high proportion of human involvement requires more inspection effort than mechanical operations.
The frequency of inspection depends on the rate at which a process may go out of control

## Slide 5: Inspection Costs
Cost
Optimal
Amount of Inspection
Cost of inspection
Cost of passing
defectives
Total Cost

## Slide 6: Where to Inspect in the Process
Raw materials and purchased parts
Finished products
Before a costly operation
Before an irreversible process
Before a covering process

## Slide 7: Examples of Inspection Points

## Slide 8: Control Chart
Control Chart
  Purpose: to monitor process output to see if it is random
  A time ordered plot representative sample statistics obtained from an on going process (e.g. sample means)
  Upper and lower control limits define the range of acceptable variation

## Slide 9: Control Chart
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
UCL
LCL
Sample number
Mean
Out of control
Normal variation due to chance
Abnormal variation due to assignable sources
Abnormal variation due to assignable sources

## Slide 10: Statistical Process Control
The essence of statistical process control is to assure that the output of a process is random so that future output will be random.

## Slide 11: Statistical Process Control
Variations and Control
  Random variation: Natural variations in the output of a process, created by countless minor factors
  Assignable variation: A variation whose source can be identified

## Slide 12: Normal Distribution
Mean




95.44%
99.74%
Standard deviation

## Slide 13: Control Limits
Sampling distribution
Process distribution
Mean
Lower control limit
Upper control limit

## Slide 14: SPC Errors
Type I error
  Concluding a process is not in control when it actually is.
Type II error
  Concluding a process is in control when it is not.

## Slide 15: Type I and Type II Errors
 | In control | Out of control
In control | No Error | Type I error (producers risk)
Out of control | Type II Error (consumers risk) | No error

## Slide 16: Control Charts for Variables
Mean control charts
  Used to monitor the central tendency of a process.
  X bar charts
Range control charts
  Used to monitor the process dispersion
  R charts
Variables generate data that are measured.

## Slide 17: Mean Chart

## Slide 18: Example

## Slide 19: Solution

## Slide 21: Range Charts

## Slide 22: Control Chart for Attributes
p-Chart - Control chart used to monitor the proportion of defectives in a process
c-Chart - Control chart used to monitor the number of defects per unit
Attributes generate data that are counted.

## Slide 24: P-chart

## Slide 27: C-chart